## Slide 1: Design of a Home Multi-Robot System for the Elderly and Disabled
Patrick Benavidez

## Slide 2: Overview
Introduction
Proposed Home Robotic System
Software and Simulation Environment
Hardware
Summary of Contributions and Completed Work
Future Work

## Slide 3: Introduction
  Demand is only increasing for assistive robots
    Japan, Europe, Korea and the US all have age-related population problems that can be helped by assistive robots
    The Robotics and Automation Society states that important research projects have been recently launched in Europe, Japan and Korea. The US is not even listed as a key player in the research. [http://www.ieee-ras.org/rehabilitation-robotics]
    Conferences: IEEE International Conference on Rehabilitation Robotics (ICORR) –2013 attendance: 340, IEEE Technologies for Practical Robot Applications (TePRA), The Rehabilitation Engineering and Assistive Technology Society of North America (RESNA) partners with ICORR
    Regular IEEE Spectrum e-articles asking “where are our home robots?”

## Slide 4: Introduction
  Demand is increasing for assistive robots (cont.)
    RoboCup added an @Home event described as “largest international annual competition for autonomous service robots and is part of the RoboCup initiative” [http://www.robocup.org/robocup-home/]

## Slide 5: Introduction (cont.)
Multiple robots and effect on task space
  Existing robot systems work in their own environment
    Roomba works as if it is the only robot in a room
    Task spaces are assumed to be the entire area
    Simple sensor beacons are used to control robots
  Task space could be split up into parts
    Make execution of task more efficient
    Robots can build sophisticated maps of the environment for navigation – could be used to partition
http://en.wikipedia.org/wiki/File:Roomba_time-lapse.jpg
    https://www.youtube.com/watch?v=S7plVfRA2jQ#t=48

## Slide 6: Introduction (cont.)
Networked and Cloud Robotics
  WillowGarage decided to make things easier for researchers with ROS and PR-2 showpiece
  Unbounded Robotics was formed by former WillowGarage employees have their UBR-1 ~$35k
Cost: ~$330k
Criticized by AARP for being too slow at folding towels and very expensive
http://unboundedrobotics.com/ubr-1/
http://www.willowgarage.com/pages/pr2/overview

## Slide 7: Introduction (cont.)
Networked and Cloud Robotics
  WillowGarage decided to make things easier for researchers with ROS and PR-2 showpiece
  Unbounded Robotics was formed by former WillowGarage employees have their UBR-1 ~$35k
  Unfortunately for Unbounded Robotics, the UBR-1 was bound to fail due to derivative work clauses in the former employee’s contracts
Cost: ~$330k
Criticized by AARP for being too slow at folding towels and very expensive
http://unboundedrobotics.com/ubr-1/
http://www.willowgarage.com/pages/pr2/overview
Unbounded Robotics was forced to close

## Slide 8: Proposed Home Robot System

## Slide 9: Proposed Home Robot System
The proposed system is designed with the following top level goals:
  Provide an application set to suit the general needs of user population
  Develop the system to be extensible and configurable
  Partition task space for heterogeneous robots

## Slide 10: Proposed Home Robot System System Extensibility & Configurability
The following principles are proposed to extend the usefulness of the system:
  Use of cloud computing technology to provide data processing support and to allow expansion of services
  Provide a set of standards allowing cooperative robot control in system
  Openness to allow application (app) driven control of robots in system
  Integration with existing equipment such as security systems and cameras, or “smart” IoT devices
Photographer: Deborah Silliman Wolfe

## Slide 11: Proposed Home Robot System System Extensibility & Configurability (Cont.)
How to manage all this in the home?
  Integration with existing equipment
Cloud Back End

## Slide 12: Proposed Home Robot System System Extensibility & Configurability (Cont.)
How to manage all this in the home?
  standards allowing cooperative robot control
Cloud Back End
  Integration with existing equipment

## Slide 13: Proposed Home Robot System System Extensibility & Configurability (Cont.)
How to manage all this in the home?
  allow application (app) driven control of robots
  standards allowing cooperative robot control
Cloud Back End
  Integration with existing equipment

## Slide 14: Proposed Home Robot System System Extensibility & Configurability (Cont.)
How to manage all this in the home?
  use of cloud computing technology
  allow application (app) driven control of robots
  standards allowing cooperative robot control
Cloud Back End
  Integration with existing equipment

## Slide 15: Proposed Home Robot System System Extensibility & Configurability (Cont.)
How to manage all this in the home?
  use of cloud computing technology
  allow application (app) driven control of robots
  standards allowing cooperative robot control
What happens when another robot is here? Will it help me?
Cloud Back End
  Integration with existing equipment

## Slide 16: Proposed Home Robot System System Extensibility & Configurability (Cont.)
How to manage all this in the home?
  Use of open-source Robot Operating System (ROS) middleware
    Provides a common API for process-to-process and machine-to-machine communication
    Provides instructions and some API to access system via non-ROS applications such as “apps” on a mobile device
    Drivers can be made for existing or legacy equipment
  use of cloud computing technology
  allow application (app) driven control of robots
  standards allowing cooperative robot control
Cloud Back End
  Integration with existing equipment

## Slide 17: Proposed Home Robot System System Extensibility & Configurability (Cont.)
How to manage all this in the home?
  Offload a portion of the work to the Internet Connected Home Portal (ICHP) and to the cloud
    Device can be similar in form to a wireless router or cable internet modem
    Maintains high bandwidth connections to robots
    Provides intermediary link between N robots and cloud computing
    Integrates with existing “smart” components
ICHP

## Slide 18: Proposed Home Robot System System Extensibility & Configurability (Cont.)
How to manage all this in the home?
  Offload a portion of the work to the Internet Connected Home Portal (ICHP) and to the cloud
    Device can be similar in form to a wireless router or cable internet modem
    Maintains high bandwidth connections to robots
    Provides intermediary link between N robots and cloud computing
    Integrates with existing “smart” components
ICHP
Internet Link to Cloud
  use of cloud computing technology
Cloud Back End

## Slide 19: Proposed Home Robot System System Extensibility & Configurability (Cont.)
How to manage all this in the home?
  Offload a portion of the work to the Internet Connected Home Portal (ICHP) and to the cloud
    Device can be similar in form to a wireless router or cable internet modem
    Maintains high bandwidth connections to robots
    Provides intermediary link between N robots and cloud computing
    Integrates with existing “smart” components
ICHP
Internet Link to Cloud
Cloud Back End
  Integration with existing equipment
  allow application (app) driven control of robots
  use of cloud computing technology

## Slide 20: Proposed Home Robot System System Extensibility & Configurability (Cont.)
How to manage all this in the home?
  Offload a portion of the work to the Internet Connected Home Portal (ICHP) and to the cloud
    Device can be similar in form to a wireless router or cable internet modem
    Maintains high bandwidth connections to robots
    Provides intermediary link between N robots and cloud computing
    Integrates with existing “smart” components
ICHP
Internet Link to Cloud
  allow application (app) driven control of robots
  Integration with existing equipment
Cloud Back End
  use of cloud computing technology

## Slide 21: Proposed Home Robot System System Extensibility & Configurability (Cont.)
How to manage all this in the home?
  Offload a portion of the work to the Internet Connected Home Portal (ICHP) and to the cloud
    Device can be similar in form to a wireless router or cable internet modem
    Maintains high bandwidth connections to robots
    Provides intermediary link between N robots and cloud computing
    Integrates with existing “smart” components
Seems fair, the workload is divided
ICHP
  standards allowing cooperative robot control
  standards allowing cooperative robot control
Cloud Back End
Internet Link to Cloud
  Integration with existing equipment
  allow application (app) driven control of robots
  use of cloud computing technology

## Slide 22: Proposed Home Robot System Set of Applications to Suit General Needs of User Population
A proof of concept set of applications are proposed to provide assistance in the following areas:
  Vision & Social
  Mobility
  Physical
  Cleaning and Safety
We propose that these tasks be split between two type of robots:
    Movement and Vision Assistance Robot (MVAR)
    Floor Cleaning Robot(FCR)

## Slide 23
Components
Manipulator arm (1)
RGB-D input device (2)
Vacuum or other cleaning device (3)
Object retrieval scoop and bay (4)
(4)
(3)
(2)
(1)
Proposed Home Robot System Floor Cleaning Robot (FCR)
FCR

## Slide 24: Proposed Home Robot System Floor Cleaning Robot (FCR)
Floor Cleaning Tasks | Driving Technology
Dirty area identification for vacuuming/sweeping/mopping | RGB-D based dirty area identification
Small object pickup | Floor RGB-D model comparison and/or database lookup
 | Mapping of house walkways
 | Manipulator mechanism and control
Self-emptying of dirt bin | Manipulator and dirt bin mechanical compatibility
 | Identification of trash can area by RGB-D
Liquid spill identification and cleanup | Spill identification
 | Mopping bar tool
 | Navigation to spill location

## Slide 25: Proposed Home Robot System Movement and Vision Assistance Robot (MVAR)
Components
Wheeled walker frame
Tablet screen UI
RGB-D camera (i.e. Kinect)
Manipulator arm
Motors
Batteries
Electronics
MVAR

## Slide 26: Proposed Home Robot System Movement & Vision Assistance Robot (MVAR)
Movement Assistance Tasks | Driving Technology
Assist in bearing weight of user | Assistive braking
 | Pressure Sensors
Passive path suggestions if obstacles block current path | Obstacle detection via RGB-D sensor and learned floor model
 | Grade detection via RGB-D and accelerometer sensors
Active path control to avoid critical obstacles and paths | Same as passive system above
 | Velocity control of platform
“Come-to-me” feature | Mapping of house walkways
 | Beacon and sensor array
 | Teleoperation
Exercise and/or rehabilitation | Pre-programmed exercises
 | Waypoint following

## Slide 27: Proposed Home Robot System Movement & Vision Assistance Robot (MVAR)
Vision Assistance Tasks | Driving Technology
Reading visual text input | Navigation/manipulation to obtain picture of text input
 | Optical character recognition (OCR) on visual input
 | Synthesize read text to speech
Reading emails out loud | Save email text to appropriate format for voice synthesis
 | Voice synthesis of digitally formatted words
Accept voice commands | Voice recognition software to decode verbal commands
 | Turn decoded commands into actions
 | Verbal Response
Zoom-in on visual input for display on large tablet screen | Optical zoom
 | Digital zoom

## Slide 28: Proposed Home Robot System Cooperative Controller
Cooperation is a necessity for household robots operating in overlapping environments with human operators involved
Current household robots like the Roomba move until they hit obstacles.
  Small scale homogeneous (swarm-style) robots colliding with one another is usually assumed to be acceptable (Roomba Fight Video)
  But this is NOT sufficient considering that safety of the user IS THE TOP CONCERN

## Slide 29: Proposed Home Robot System Cooperative Controller
Example situations will be encountered where MVAR and FCR should work together:
  MVAR crosses paths with FCR in a projected trajectory (pictured)
  FCR finds a dirty area under MVAR frame
  Transporting items picked up by FCR to MVAR to user/operator

## Slide 30: Proposed Home Robot System Cooperative Controller
Policies need to be established for situations where cooperation is either beneficial in terms of:
  safety (to prevent operator injury)
  cost reduction (to use smaller cheaper components, i.e. smaller robotic arms) and sharing across both platforms

## Slide 31: Proposed Home Robot System Cooperative Controller
Cooperative Controller Tasks | Driving Technology
Robot-to-Robot coordination of navigation actions | Swarm-based simulation of intended paths for collision detection and flagging
 | Task priority driven decision making
 | Communication of actions via wireless radio
Human-to-Robot coordination of robot-to-human navigation actions | Human detection and tracking
 | Verbal/visual/non-verbal communication of action to human
 | Safety driven decision making
Human-to-Robot coordination of coupled Robot-to-Robot actions | Communication to begin action
 | Navigation to close proximity
 | Identification of manipulation action

## Slide 32: Software and Simulation Environment

## Slide 33: Software and Simulation Environment
Software | Name and Version | 
Operating System | Ubuntu Linux 12.04 LTS | 
Robot Middleware | Robot Operating System (ROS) (Hydro Release) | 
Image Processing | OpenCV 2.4.6 (ROS Hydro Release Version) | 
3D Point Cloud Processing | PCL 1.7.0 (ROS Hydro Release Version) | 
3D Simulator | ROS Gazebo Simulator 1.5? | 

## Slide 34: Hardware

## Slide 35: Hardware – FCR
http://en.wikipedia.org/wiki/Kinect
http://dn.odroid.com/homebackup/XU3LiteMain.jpg
Roomba Discovery (circa 2004)
Very early prototype
More rigid 3D printed prototype

## Slide 36: Hardware – MVAR
http://en.wikipedia.org/wiki/Kinect
http://dn.odroid.com/homebackup/XU3LiteMain.jpg
Nova GetGo Walker
SolidWorks model by UTSA’s Eric Wineman
Design to be completed soon

## Slide 37: Hardware - Infrastructure
UTSA Cloud-
Research Data Center
(RDC)
Trendnet Wireless IP Camera
http://www.linksys.com/images/productmt/834023/372.jpg

## Slide 38: Summary of Contributions and Completed Work

## Slide 39: Completed Work
Modifications to drive a salvaged iRobot Roomba in ROS
  Wired motor drivers and Arduino microcontroller to computer
  Added lithium polymer battery for extended use
  Added Kinect and related hardware
  Added an embedded ODROID Xu3 computer with 8 cores in big.LITTLE configuration
  3D Printed and assembled under-actuated gripper
  3D Printed many components of robot base ~200 printing hours

## Slide 40: Completed Work
3D point cloud data processing
  Now very experienced in PCL software
  Methods to filter, geometrically transform to fix orientation, and process data
RGB+D image processing
  Calibrated cameras of the Kinect
  Software developed to acquire and process both RGB & D images in ROS for processing

## Slide 41: Completed Work
Commercial cleaning motions & control examples

## Slide 42: Completed Work
ROS on the Cloud
  Feature matching for Visual SLAM via ROS-based mechanism similar to MPI
  Implemented the network setup for successful experimentation

## Slide 43: Future Work

## Slide 44: Future Work
    *Custom designs using 3D printed parts from ACE Lab’s soon-to-be acquired 3D printer
MVAR
  Add manipulator arm*
  Simulation on Home State Recognition
  Experiment on Passive and Active Navigation
FCR
  Add manipulator arm*
  Simulation on FCR Small Item Detection
  Experiment on FCR Cleanup of Small Liquid Spill
Cooperative Controller
  Simulation on Robots Crossing Paths
  Experiment on Small Object Handoff
ICHP

## Slide 45: Simulations
Home State Recognition
  Goals:
    1) Detect states of light switches in a room.
    2) Detect state of deadbolt locks.
  Limitation: Use of datasets taken in apartment and in ACE Lab of light switches
  Time permitting: the simulation will become an experiment with live detection of the switch state

## Slide 46: Experiments
MVAR Passive and Active Navigation
  Goal: Navigate through an environment typical to that of a household.
  Limitation: dataset only from apartment, experiment in ACE Lab
MVAR with User
Good Path for MVAR
Obstacles
Water Spill
Hard Floor
Destination

## Slide 47: Questions?

## Slide 48: Contributions
This work contributes following five items to the field of home robotics:
  A new concept for a home multi-robot system for elderly care
  Methods and system for a Floor Cleaning Robot (FCR)
  Expansion of multi-robot system thinking to home robots with robot/human and robot/robot interactivity
  Methods and system for a Movement and Vision Assistance Robot (MVAR)
  A cooperative controller for enabling and organizing multi-robot interaction.

## Slide 49
Controllers
High Level Controllers
(Clean Area Avoidance, Small Object Manipulation, Cooperative Controller)
Low Level Controllers
(Obstacle Avoidance, Motion planning)
External Actors
Environment
Sensor Data
Onboard Sensors
(Distance,
Velocity, Position, Force)
External
Observer
Actuation
Robot’s
Actions
Desired Actions & Reactions
Robot
Actions
External
Controller
Robot
External Computer
Environmental
Other Robot
Proposed Home Robot System Floor Cleaning Robot (FCR)

## Slide 50: Proposed Home Robot System Movement & Vision Assistance Robot (MVAR)
Controllers
High Level Controllers
(Path Controller, Cooperative Manipulation Controller, Cooperative Path Controller)
Low Level Controllers
(Obstacle Avoidance, Motion planning, Braking)
External Actors
Environment
Sensor Data
Onboard Sensors
(Heading, Distance,
Velocity, Position, Force)
External
Observer
Actuation
Robot’s
Actions
Desired Actions & Reactions
Robot
Actions
External
Controller
Robot
External Computer
Environmental
Other Robot