## Slide 1: Vision Based Cloud Robotics
Mohan Muppidi, Joaquin Labrado
ACE Laboratory, UTSA

## Slide 2: Overview (cntd..)
Image Transfer
Robot
Cloud
Start

## Slide 3: Introduction
Two questions help humans navigate their environment
“What does the world around me look like?”
“Where am I in this world”
This problem of navigation is often solved with
Simultaneous Localization And Mapping (SLAM)
If odometry and localization are based on image data then it is called Visual SLAM or VSLAM in short.

## Slide 4: Introduction (cntd..) Applications
Asimo robot
Jibo robot
Nao robot
Dyson 360 eye
Dyson 360 eye navigation
Personal Robots
Vacuum Cleaning Robots
Assistive robots
Robotic guides in Museums
Assistive robots in Libraries
Unmanned Aerial Vehicles

## Slide 5: Container based SLAM
Humans easily remember complex objects (such as trees, signboards or shops) as landmarks.
Robot remembering or storing such complex objects is not only computationally expensive but also time consuming.
Similar to how humans navigate their environment this research uses images to also identify landmarks.
World is divided into a grid with 1x1 blocks. Each grid is treated as a container with landmark images.
For ease of localization these blocks are grouped to follow a convention

## Slide 6: Container based SLAM (cntd..)
Odometry of robot can be determined by
IMU
Encoders
Visual Odometry etc.
Images are treated as landmarks. Each container has 8 landmark images covering the 360⁰ view of robot
Naming convention is followed so that coordinates of that container can be determined from the name itself

## Slide 7: Container based SLAM (cont..)
Illustration of levels in landmark database
360⁰ robot view divided into 8 segments
Level 0

## Slide 8: Localization
Localization
“Where am I in this world ?”
Localization helps robot to know its current location in an environment with respect to base frame
Advantage of the localization algorithm is that the landmark database created using Container based SLAM can be used to localize any robot
Image feature matching based localization

## Slide 9: Experiment
The experiment was conducted on the 2nd floor hallway of UTSA Bio Sciences and Engineering building. The experiment started and ended at same location with the hallway as shown below

## Slide 10
Landmark Database created using SLAM

## Slide 11
Localization of Robot based on previously built database

## Slide 12: CLOUD BASED LOCALIZATION
Limitations of Localization Algorithm
The robot has to be in immediate or next neighborhood of the previous location before next sample is taken
If not in this area then full database has to be searched, Time consuming and slows down the robot.
Overcoming the Limitations
Performing parallel search
Offloading some computing from on board computer

## Slide 13
Illustration of cloud based parallel processing using ROS

## Slide 14: Time comparison between results with parallel algorithm and serial algorithms
Serial Algorithm results
8.23 seconds per 100 frames
Without any manipulation such
as resizing or cropping on
Database images
Parallel Algorithm results
1.84 seconds per 100 frames
Without any manipulation such as resizing or cropping on database images
77%

## Slide 15: Quadrotors
Fly through the use of 4 motors
Many different applications
  Swarms
  Eye in the Sky

## Slide 16: Quadrotors
In the Lab
  ARDrone 2.0
  Parrot Bebop
  Erle Copter

## Slide 17: Formation Control
Multiple UAS's flying and moving as a group
Useful for localization
SAR applications

## Slide 18: Formation Control in the Lab
4 total quadrotors in a formation
Use of cameras to keep formations
Implement SLAM

## Slide 19: 3D Depth Cameras
LiDAR
RGB-D data

## Slide 20: 3D Depth Cameras
Xbox Kinect
Asus XTION PRO

## Slide 21: Use of the Xbox Kinect
Point clouds

## Slide 22: Use of the Xbox Kinect
Depth Data for controllers