## Slide 1: Task Allocation for Cooperative Multi-agent Systems
Advisor:
Dr. Karimoddini
Laya Shamgah
PhD Student
ACCESS

## Slide 2: Outline
ACCESS
1
Introduction to Cooperative Control
3
Problem of Task Allocation
4
Existing Approaches
Future Plan
5
Applications
2

## Slide 3: Examples of Cooperation in Nature
ACCESS
Flocking of Birds
Schooling of Fish

## Slide 4: Advantage of Cooperative Control
Cooperation is being used to accomplish some common purpose that is greater than the purpose of each individual.
ADVANTAGES
Faster task completion
More flexible solution
Completion of the task impossible for single agent
Increased robustness
ACCESS

## Slide 5: Applications of Cooperative Control
Crowd Dynamics and Building Egress
Mobile Robot Networks
ACCESS

## Slide 6: Applications of Cooperative Control
Autonomous Formation Flying and UAV Networks
ACCESS
Multi-Robot Remote Manipulation

## Slide 7: Challenges of Cooperative Systems
Challenges
Issues
Dynamic events
Changing task demands
Resource failures
Presence of adversaries
Limitation in environment (Limited time, energy, computation, communication
Limitation in individuals capabilities (Limited sensing and mobility)
Formulation, description, decomposition and allocation of tasks
Communication languages and protocols
Coherence, Stability behavior, …
Task allocation
ACCESS

## Slide 8: Task Allocation Problem
Which individual should execute which task in order to cooperatively achieve the global goal?
better TA more efficient performance
Complexity arises with:
  Larger team sizes
  Greater heterogeneity of robots and tasks
ACCESS

## Slide 9: Task Allocation Problem
Agent 1
Agent 3
Global Task
Agent 2
Subtask1
Subtask2
Subtask3
ACCESS

## Slide 10: Different Types of Tasks
Single
Multiple
Discrete
Continuous
Time-scaled
Static
Dependent
Independent
ACCESS

## Slide 11: Task Allocation Approaches
Self-organizing approaches
Threshold-based methods
Game theoretical methods
Planning-based approaches
Market-based methods
DES task-decomposition methods
ACCESS

## Slide 12: Task Allocation Approaches
Self-organizing approaches
DES task-decomposition methods
Market-based methods
Planning-based approaches
Game theoretical methods
Threshold-based methods
ACCESS

## Slide 13: Self-organization Approaches
Local communication
Limited communication
Group interaction
Restricted individuals capabilities
Self-interested agents
Feasible individual decision
No centralized or decentralized control
  Self-organizing systems rely on group behaviors to emerge from group interactions and individual decision making based on local data.
ACCESS

## Slide 14: Self-organization Approaches
Global Task
Subtask1
Subtask2
Subtask3
(1) Decomposition
Agent 1
Agent 2
Agent 3
(2) Decision making
Decision process
Decision process
Decision process
(3) Task allocation
ACCESS

## Slide 15: Task Allocation Approaches
Self-organizing approaches
Threshold-based methods
Game theoretical methods
Planning-based approaches
Market-based methods
DES task-decomposition methods
ACCESS

## Slide 16: Threshold-based TA Methods
  if
  decision criteria > threshold
  agent picks the task
Decision process
Agent 1
  Decision to select a particular task depends on:
  Individual’s perception of a task
  Individual’s response threshold for the task:
  Threshold types:
  Same fixed response threshold for all agents
  Different fixed response threshold based on individuals capabilities or the configuration of the system
  Adaptive response-threshold models change the thresholds over time
ACCESS

## Slide 17: Problem Formulation
  Robotic manufacturing shop-floor scenario:
Tasks:
  Each task represents a machine capable of producing goods from raw materials.
  The machines require regular maintenance work.
  Together the production and maintenance work loads constitute the total workload or task urgency.
Individuals:
  Represent the robots.
  The robots repeatedly select tasks and if the robot is outside a fixed task boundary, it navigates towards the task. If the robot is within the task boundary it remains there until the end of the time step when a new (or the same) task is selected.
ACCESS

## Slide 18: Problem Formulation
At each time step, each machine requires a minimum threshold, μ, number of robots to service the total workload, . Without this number of robots present the urgency will keep increasing.
Manufacturing operation split into two phases:
  the production phase, which includes production and maintenance tasks,
  the maintenance phase, which contains maintenance tasks only.
A machine starts out in the production phase with a given production work load, . When there is no production work left, it enters the maintenance phase. During both phases, denotes the amount of maintenance work incurred in a single time-step if an insufficient number of robots serve a task. Correspondingly we denote the decrease in the total workload by .
ACCESS

## Slide 19: Problem Formulation
If no robot attends a machine, on each time-step a constant maintenance workload of will be added to to increase its task urgency. If t time steps pass without any production work being done, the task urgency at time-step t would have increased as follows:
If the required number of robots attend a machine, there is no extra maintenance work. Instead, the task urgency of this machine will decrease by . If robots work on a machine simultaneously at time step t, this decrease will be: × . In such cases, task-urgency at time step t + 1 is given by the following equation
ACCESS

## Slide 20: Problem Formulation
: production completion time
For a particular machine j, once reaches zero, there is no more production work left and this time step t gives us the .
: the average production completion time of a shop floor
: the theoretical minimum number of time steps necessary to finish production works
: production completion delay
ACCESS

## Slide 21: Task Allocation Approaches
Self-organizing approaches
Threshold-based methods
Game theoretical methods
Planning-based approaches
Market-based methods
DES task-decomposition methods
ACCESS

## Slide 22: Game Theory Definitions
Game:
  Situation in which players (participants) make strategic decisions that take into account the actions and reactions of the other players
Cooperative Game:
  A game in which players can make binding commitments
Non-cooperative Game:
  A game in which binding commitments are not possible
Payoff:
  Value of an outcome to a player
Strategy:
  Rule or plan of action for playing a game; one player’s best response to each action taken by other players
ACCESS

## Slide 23: Game Theoretical Approaches
Global Task
Subtask1
Subtask2
Subtask3
(1) Decomposition
Agent 1
Agent 2
Agent 3
(2) Playing game
(3) Task Allocation
Game rules
Game rules
Game rules
ACCESS

## Slide 24: Problem Formulation
The problem is modeled as a hedonic coalition formation game between the agents and the tasks that interact in order to form disjoint coalitions.
A coalition formation game is classified as hedonic, if
The payoff of any player depends solely on the members of the coalition to which the player belongs.
The coalitions form as a result of the preferences of the players over their possible coalitions’ set.
ACCESS

## Slide 25: Coalitions in Hedonic Games
Central concepts:
: Finite set of players
Coalition = non-empty subset of
Partition divides N into disjoint coalitions
denotes coalition in containing player
Every player ranks all the coalitions containing via and
A coalition blocks a partition , if all players have and hence strictly prefer being in to being in current coalition
A partition is core stable, if there is no blocking coalition .
ACCESS

## Slide 26: Coalitions in Hedonic Games
Example:
Three players
Preferences of player
Preferences of player
Preferences of player
Partition not core stable: blocks
Partition , not core stable: blocks
Partition , not core stable: blocks
Partition , not core stable: blocks
Partition , , not core stable: blocks
This simple cyclic 3-player game does not allow a core stable partition.
ACCESS

## Slide 27: Pros and Cons
Pros
Better scale-up than planning methods
Difficult to predict the exact behavior of Individuals
Cons
Rely less on modeling the environment, tasks and individuals
Make decision based on local data
Approaches mainly focus on single global tasks
Difficult to formally design, analyze and implement
ACCESS

## Slide 28: Task Allocation Approaches
Self-organizing approaches
Threshold-based methods
Game theoretical methods
Planning-based approaches
Market-based methods
DES task-decomposition methods
ACCESS

## Slide 29: Market-based Approaches
Global Task
Subtask1
Subtask3
(1) Decomposition
Agent 1
Agent 2
Agent 3
bid1
bid2
bid3
(2) Offer and bid
Subtask2
bid2 > bid 1 , bid3
(3) Negotiation
(4) Task allocation
ACCESS

## Slide 30: Auction Types
1. Single-item auction:
only one item is offered
each participant submits a bid
auctioneer awards the item to the highest bidder
2. Multi-item auction:
multiple items are offered
participants can win at most one item apiece
3. Combinatorial auction:
multiple items are offered
each participant can bid on any combination of items.
ACCESS
  more centralized: more decentralized:
  quality of solution speed of solution
Centralized
Decentralized

## Slide 31: Pros and Cons
Pros
Intuitive and straightforward for design and implement
Performance is reduced if number of agents arises
Cons
Strong communication requirements
Tradeoff between speed and quality
ACCESS

## Slide 32: Task Allocation Approaches
Self-organizing approaches
Threshold-based methods
Game theoretical methods
Planning-based approaches
Market-based methods
DES task-decomposition methods
ACCESS

## Slide 33: Discrete Event System
Complex mathematical model
DES model
transitions
states
Mathematically convenient models
A flexibility to model various levels of detail and complexity
Allowing the modeling of uncertainty and dynamic (time changing) systems
Advances and variety in DES software
ACCESS

## Slide 34: DES Cooperative Control
Global Task
Subtask1
Subtask2
Subtask3
Formal task decomposition
Supervisory control1
Supervisory control2
Supervisory control3
(2) Controllers design
Agent 1
Agent 2
Agent 3
ACCESS

## Slide 35: Problem Formulation
Agent 1
Agent 2
Agent 3
Agent 4
Global task
Subtasks
Individuals
Problem: Given a deterministic task automaton with event set and local event sets , , what are the necessary and sufficient conditions that is decomposable with respect to parallel composition and natural projections , , such that ?
ACCESS

## Slide 36: Future Plan
Objective:
Obtain a decentralized, near-optimal and formal method for task allocation in search and coverage problems by combining task decomposition methods, DES models and game theory
Game theory
DES method
Formal procedure
Search and coverage problem
ACCESS

## Slide 37: Why Search and Coverage Problem?
The use of robots in surveillance and exploration with minimal human supervision or intervention is gaining prominence.
As the number of vehicles increases it becomes increasingly difficult and even impossible for direct human supervision.
Typical applications include air- and ground-based mapping of predetermined areas for tasks such as surveillance, target detection, tracking, and search and rescue operations.
The use of multiple collaborative robots is ideally suited for such tasks.
ACCESS

## Slide 38: Why DES?
  Rapid evolution of computing, communication, and sensor technologies has brought about the proliferation of new dynamic highly complex systems (Example: computer and communication networks; automated manufacturing systems; air traffic control systems; advanced monitoring and control systems in automobiles or large buildings; intelligent transportation systems; distributed software systems, etc.)
  DES has emerged to provide a formal treatment of such man-made systems
  The challenge is to develop new modeling, analysis and design techniques, and systematic control and optimization procedures for this new generation of systems
  Discrete event systems is a growing field that utilizes many interesting mathematical models and techniques.
ACCESS

## Slide 39: Why Game Theory?
  To jointly satisfy all three of the requirements of agility and robustness, timeliness and high-quality solutions for search and coverage problems
  negotiation protocol allows to spread the computational burden of solving the problem across the agents in the system, which adds to the control mechanism’s robustness and the timeliness of its solutions
  Better scale-up than other methods
  Rely less on modeling the environment, tasks and individuals
  Make decision based on local data
ACCESS

## Slide 40
Thank you
Any Question?
ACCESS

## Slide 41: Refrences-1
“A comprehensive taxonomy for multi-robot task allocation” G. Ayorkor Korsah, Anthony Stentz2 and M. Bernardine Dias.
“A Formal Analysis and Taxonomy of Task Allocation in Multi-Robot Systems” Brian P. Gerkey and Maja J. Mataric.
“Self-organized Task Allocation to Sequentially Interdependent Tasks in Swarm Robotics” A.Brutschy, G.Pini, C.Pinciroli, M.Birattari, and M.Dorigo.
“Local interactions over global broadcasts for improved task allocation in self-organized multi-robot systems” Md Omar Faruque Sarker, Torbjørn S. Dahl, Elsa Arcaute, Kim Christensend.
“Hedonic Coalition Formation for Distributed Task Allocation among Wireless Agents” W. Saad, Z. Han, T. Basar, M. Debbah, and A. Hjørungnes.
“Autonomous Vehicle-Target Assignment: A Game-Theoretical Formulation” Gürdal Arslan, Jason R. Marden, Jeff S. Shamma.
“Decentralized Dynamic Task Allocation Using Overlapping Potential Games” Archie C. Chapman1,∗, Rosa Anna Micillo2, Ramachandra Kota1 and Nicholas R. Jennings1.
“Market-Based Multirobot Coordination: A Survey and Analysis”, M. Bernardine Dias, Robert Zlot, Nidhi Kalra, and Anthony Stentz, Proccessings of IEEE.
“Cooperative Tasking for Deterministic Specification Automata”, Mohammad Karimadini, Hai Lin, Ali Karimoddini, Asian Journal of Control, Vol. 00, No. 0, pp. 1-14, Month 2008.
ACCESS

## Slide 42: Refrences-2
“Decentralized Hybrid Formation Control of Unmanned Aerial Vehicles”, Ali Karimoddini, Mohammad Karimadini, Hai Lin, American Control Conference (ACC) June 4-6, 2014. Portland, Oregon, USA.
“Guaranteed global performance through local coordinations”, Mohammad Karimadini, Hai Lin, Automatica 47 (2011) 890–898.
“Market-Based Coordination of UAVs for Time-Constrained Remote Data Collection and Relay”, Ajorlou, A., Homaifar, A., Esterline, A., Moore, J. G., and Bamberger, R. J..
“Modeling and control of logical discrete event systems”, Ratnesh Kumar, Vijay K. Garg, SPRINGER SCIENCE+BUSINESS MEDIA, LLC.
“Introduction to Discrete Event Systems”, Christos G. Cassandras, Stéphane Lafortune, 2nd Edition, Springer.
“Cooperative Air and Ground Surveillance A Scalable Approach to the Detection and Localization of Targets by a Network of UAVs and UGVs”, BEN GROCHOLSKY, JAMES KELLER, VIJAY KUMAR, AND GEORGE PAPPAS , 16 IEEE Robotics & Automation Magazine 1070-9932/06/$20.00©2006 IEEE SEPTEMBER 2006
“Cooperative Control of UAVs for Search and Coverage”, Ali Ahmadzadeh, Gilad Buchman, Peng Cheng, Ali Jadbabaie, Jim Keller, Vijay Kumar , and George Pappas,
ACCESS